## Slide 1
Bridge Structural Health Monitoring
Kasireddy Vadicherla · X25104047
Road authorities assess bridges by visual inspection on a cycle measured in years — while the deck keeps working, strain cycles and thermal joint movement accumulate unseen every day.
Years between inspections
24/7 strain accrues
0 visibility in the gap

## Slide 2
What I Built — Bridge to Browser
Span sensors
10 · 2 spans
Fog node
windows · 4 thresholds
Amazon SQS
batched summaries
AWS Lambda
python3.12 ingest
DynamoDB
time-keyed store
API GW + S3
integrity index
Every 10-second window becomes one min/max/average per sensor, checked against four thresholds at the fog node; the dashboard folds each span into a 0-100 integrity index.

## Slide 3
Live Demo
bshm-frontend-661886400169.s3.us-east-1.amazonaws.com
1
A 0-to-100 integrity index per span
The dashboard folds each span's strain average and peak vibration into one structural integrity index, live on read.
2
Two spans, tracked live
Span-A reads 100 percent with no active alerts and Span-B reads 76.8 percent, good and tracking real readings.
3
The index reaches zero where an alert fires
Its critical bound equals the alert threshold, so the number and the alarm agree by construction.

## Slide 4
Hardest Part — one risky Terraform apply
Problem
Every project here deploys through one shared Terraform module, and its local state file already tracked a different live AWS stack under the default workspace. Nothing in my code was wrong — but applied against that workspace, Terraform reconciles state and plans to destroy the other deployment's live resources. The only warning is one line of plan output.
Solution
A dedicated workspace was created first, and the re-plan read "24 to add, 0 to change, 0 to destroy"; then a single apply built all 24 resources, healthy within a minute. Never apply an unread plan. The same pre-deploy audit also caught two silent defects — a pagination undercount and unbatched publishing — both fixed and regression-tested before launch.