## Slide 1
Elevator & Escalator Fleet Monitoring
Rasool Basha Durbesula · X24205478
A lift fails two ways — slowly, as a motor creeps hot or a ride roughens, and suddenly, as one overweight trip loads the car past its limit — and a clipboard round sees only one instant.
Motor > 85 °C (avg)
Overload > 1,000 kg (peak)
Stall < 0.5 m/s
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Sensor to Screen
EDGE
Cab sensors
10 · 2 towers
Fog node
window · aggregate · alert
CLOUD (serverless)
Amazon SQS
aggregate queue
AWS Lambda
nodejs20 ingest
DynamoDB
window store
API GW + S3
fleet dashboard
Each rule reads the number its fault lives in — the drift faults read the window average, the single-instant overload reads the window maximum.

## Slide 3
Live Demo
eef-frontend-786504441742.s3.us-east-1.amazonaws.com
1
A meter card per signal, per tower
Motor temperature, door cycles, cab vibration, load weight and travel speed live for both towers with native meter bars.
2
Two faults at opposite ends of time
Tower-B is firing a ride-quality fault (a drift, read on the average) and an overload warning (an instant, read on the peak) at once.
3
Window-average trend charts
Five trend charts run per tower, so a slowly overheating motor is visible on the trend well before it alarms.
Switch to the live dashboard here — backup video ready.

## Slide 4
Hardest Part — peak or trend
Problem
Every window becomes the same five numbers: count, min, max, average, latest. If every rule read the average, the overload would slip through — one overweight trip among nine ordinary ones averages out below the limit while the car is genuinely overloaded.
Solution
Bind each rule to the number its fault lives in: overheating, rough riding and stalling are trends, so they read the window average; overload is a single instant, so it reads the window maximum. The samplers are drift-corrected so every window covers a like span of time and the peak that trips an overload is real, not a clock artefact. A unit test fires the overload on a peak the average leaves below the limit.