## Slide 1
Patient Vitals Remote Monitoring
Sri Venkat Bora · X25164414
Ward rounds are periodic, but deterioration is a trend — falling oxygen or a climbing heart rate develops over minutes, so a single reading in isolation can still look normal.
SpO₂ < 92% alert
5 vitals · 2 patients
10 s alert window
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Bedside to Cloud
Bedside sensors
10 streams · 2 patients
Fog gateway
10 s windows · clinical rules
Amazon SQS
batched aggregates
AWS Lambda
nodejs20 ingest
DynamoDB
windowed records
API GW + S3
ward dashboard
EDGE
CLOUD
Alert decisions happen at the bedside gateway; the cloud receives compact aggregates, not raw vital streams.

## Slide 3
Live Demo
fpv-frontend-457516959142.s3.us-east-1.amazonaws.com
1
Two patients, five vitals live
Heart rate, SpO2, respiration, temperature and blood pressure streaming for both beds, each checked against its clinical limit as it lands.
2
A hypoxia alert on real data
The banner raises as Patient-1's SpO2 crosses the 92% trigger — captured live at 89.7% — not a scripted demo value.
3
The pipeline is genuinely live
The stored-record count climbs between refreshes and the freshest reading stays a couple of seconds old, so nothing here is cached.
Switch to the live dashboard here — backup video ready.

## Slide 4
Hardest Part — a bug no local test could catch
Problem
The fog gateway's queue publisher shipped with the emulator's fake access keys hard-coded into every connection. Locally everything worked — the emulator accepts any credentials, so all 41 tests and the end-to-end check stayed green — but on real AWS every send would be rejected the moment it deployed.
Solution
Fake keys are now attached only when an emulator endpoint is configured; on real AWS the SDK falls back to its own identity chain. A cloud-readiness audit caught two more emulator-only assumptions the same way, and new regression tests lock all three fixes in.