## Slide 1
Industrial Equipment Predictive Monitoring
A fog-to-cloud pipeline that watches five machine signals and raises alarms at the edge
Vikas Reddy Amanagantti
Student ID X25178849
MSc in Cloud Computing · Fog and Edge Computing (H9FECC)
National College of Ireland

## Slide 2: Why periodic checks miss the failure
A walk-round inspection reads each gauge once; the fault develops in the minutes between rounds and keeps developing until the next one.
Machine failure rarely shows on one dial: it builds across heat, vibration, bearing noise, speed and power draw at the same time, five signals no walk-round reads together.
Two production lines run in parallel, and each motor needs its own watch: line 1 running cool says nothing about line 2.
By the time a person notices, the machine has been damaging itself the whole time nobody was looking.
Motor temperature alarm limit is 95 degrees C: a winding can sit above it all shift between manual rounds.
Vibration alarm limit is 7 mm/s: drift toward it builds in minutes, not inspection cycles.
Rotation overspeed limit is 3,400 RPM, with an underspeed alarm at 1,000 RPM on the same shaft.

## Slide 3: How it works
Machine sensors: ten sensor units across two production lines, five signal types.
Fog node: windows 10 s of readings, aggregates, and raises alarms at the edge.
Queue on Amazon SQS: one compact aggregate per window, buffered for the cloud.
Serverless ingest on AWS Lambda: consumes the queue and reshapes each record.
Store on Amazon DynamoDB: keyed by sensor type and site, ready to query.
Live dashboard: site served from Amazon S3, data via Amazon API Gateway.
Runs end-to-end today on Docker with an AWS emulator standing in for the cloud services; moving to real AWS is one scripted deployment step, using the same cloud interfaces throughout.

## Slide 4: Demonstration highlights
Live dashboard from the running stack: a card per signal with its current reading, real alarm limit and trend, with a health footer along the bottom.
The end-to-end check confirms every one of the five signal types lands in the datastore.
Pipeline health checks: 4 of 4 green across fog gateway, queue, Lambda and data flow.
94 automated tests pass across the sensors, fog, processor and dashboard modules.
A 2,000 message burst absorbed in a load test with 32 senders in parallel.

## Slide 5: Hardest part: sealing a window under concurrent writes
The problem:
  Sensor posts arrive on several web-server threads while a timer has to seal the ten-second window on its own thread, and both touch the same buffer.
Why it was hard:
  Holding a lock across the whole window close stalls every arriving reading behind the summary work; dropping the lock loses or double-counts a reading that lands right on the boundary.
The fix:
  Take the lock only long enough to swap the filled buffer aside and install an empty one, then release it and do all the aggregation and alarm evaluation on the swapped-out copy outside the lock.
The hot ingest path never waits on a slow window close, and every reading still lands in exactly one window.

## Slide 6: Takeaways
Decide at the edge:
  Alarms fire at the fog node inside a ten-second window; the cloud receives one compact aggregate per window, not a firehose of raw readings.
Serverless backbone:
  Amazon SQS, AWS Lambda and DynamoDB carry the cloud side; they scale with load and leave no servers to patch or babysit.
Ready for real AWS:
  Verified end-to-end on the local stack, 42 tests green, and one scripted step from the real cloud, with the bug that would have broken that move already gone.
Thank you. Questions?