## Slide 1
Wildfire Forest Monitoring
Deekonda Rakshan · X25180754
Fire weather compounds quietly — heat, smoke, wind and drying soil each look tolerable alone; the danger is the combination, and it can develop between two routine checks.
Heat alarm 42 °C
Risk climbs from 30 °C
1 s smoke samples
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Forest Edge to Cloud
Field sensors
10 · 2 stations · 5 metrics
Fog node
windows · fire alerts
Amazon SQS
batched sends
AWS Lambda
nodejs20 ingest
DynamoDB
window history
API GW + S3
0–4 risk dial
EDGE
CLOUD
Windowing, aggregation and fire alerts run beside the sensors, so warnings never wait on the cloud; a 0-to-4 fire-risk dial is derived per station on read.

## Slide 3
Live Demo
wfm-frontend-923613097540.s3.us-east-1.amazonaws.com
1
A 0-to-4 fire-risk dial per station
The dashboard grades each ranger station on read from earlier, lower thresholds — an escalation gradient ahead of any hard alarm.
2
A smoke-density trend per station
Both stations' smoke charts run live, so a rising smoke plume is visible on the trend before it trips a hard alert.
3
A fire-detection alert on a smoke spike
Drive smoke density up on one station and the fire-detection alert fires within a window, dial climbing toward 4.
Switch to the live dashboard here — backup video ready.

## Slide 4
Hardest Part — an invisible credential bug
Problem
Locally the pipeline signs its queue and database calls with the emulator's dummy credentials, and it decided when to use them by checking whether an AWS access-key variable was present. But real AWS injects that exact variable into every function it runs — so in production every call would be signed with incomplete credentials and rejected. All 95 tests stayed green; nothing could fail until the first real deployment.
Solution
Gate on a signal that only exists locally: the emulator's endpoint address. On real AWS it is absent, so the platform's own credentials take over automatically. New tests now pin that behaviour down in both profiles.