## Slide 1
Offshore Wind Farm Turbine Monitoring
Vishvaksen Machana · X25173421
Turbines are reached by boat and visits can be weeks apart — a bearing overheating or a gearbox losing lubrication pressure stays invisible until the next scheduled inspection.
Gearbox < 2.5 bar
10 streams · 2 turbines
edge alert rules
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Sea to Cloud
Turbine sensors
10 streams · 2 turbines
Fog gateway
windows · 4 rules
Amazon SQS
1 batched call / cycle
AWS Lambda
nodejs20 ingest
DynamoDB
time-ordered store
API GW + S3
live dashboard
Four condition rules run at the edge, so a fault is flagged in the same window it appears; only compact summaries cross the limited sea link.

## Slide 3
Live Demo
owf-frontend-015611713565.s3.us-east-1.amazonaws.com
1
Both turbines, five metrics
Wind speed, blade vibration, generator temperature, power output and gearbox pressure live for both turbines.
2
Gearbox pressure on the window minimum
A momentary dip below 2.5 bar is a lubrication fault — the rule reads the worst reading in each window, so a single dip cannot hide in an average.
3
A cross-turbine power trend, climbing live
The power chart tracks both turbines together, and the stored count climbs 17 to 132 to 204 across refreshes, so the data is genuinely live.

## Slide 4
Hardest Part — the credential trap
Problem
Two cloud-facing modules decided they must be in local testing whenever the standard access-key variable was present, and swapped in fake, emulator-only credentials. But the serverless platform always injects that same variable to deliver a function's real credentials — so in production both functions would discard their real identity and fail their first call, while every local test kept passing. The same signal meant opposite things in the two environments.
Solution
Gate on the local-emulator endpoint variable instead — the one signal that genuinely means local. Deployed functions now fall through to the platform's default credential chain and pick up their real execution-role identity. A pre-deployment audit caught this plus two more; all three were fixed before the first deploy, and every health check was green on the first live poll.