## Slide 1
Public Transit Fleet Monitoring
Real-time bus telemetry from two depots, aggregated at the edge, stored serverlessly
MSc in Cloud Computing · Fog and Edge Computing (H9FECC)
National College of Ireland

## Slide 2: Why periodic fleet checks fail
A bus's condition changes minute by minute while it is on the road, but a depot inspection only sees the vehicle once it is parked.
Faults develop mid-route: engine overheating and brake wear build up during service, so by the evening walk-around the damage is hours old.
Some problems cannot wait: overcrowding and low fuel need a response now, not a line in the end-of-shift report.
Too much to watch by hand: five metrics per depot across two depots is ten continuous telemetry streams, far more than staff can reliably eyeball.
10 live telemetry streams.
4 safety alert rules at the edge.
2 depots, one shared fog gateway.

## Slide 3: How it works: edge to serverless cloud
Bus sensors: engine temp, brake wear, passengers, fuel and speed, five streams per depot.
Fog gateway: windows and aggregates each stream, and checks four safety rules at the edge.
Queue (Amazon SQS): carries one compact aggregate per window, not raw readings.
AWS Lambda: serverless ingest that consumes the queue and batch-writes records.
Amazon DynamoDB: time-ordered store of per-window fleet records.
Live dashboard: per-depot fleet cards and trends, served by S3 and API Gateway on AWS.
Verified end-to-end locally on Docker and LocalStack, an AWS emulator, and deploys to AWS with a single scripted step.

## Slide 4: Demonstration highlights
Live dashboard during the local demo run: all four pipeline health checks green (top right) and a real overcrowding alert firing for depot-a.
130 automated tests pass across the four modules.
2,000 message burst absorbed in the load test, using 32 parallel workers.
4/4 health checks green: gateway, queue, Lambda, pipeline.

## Slide 5: The hardest part and how it was solved
The problem:
  Ten sensor streams post readings to one fog gateway while, at the same moment, a timer thread drains the buffer to build the window aggregates. Every reading must survive that handover.
Why it is hard:
  A reading dropped in the race does not crash anything; the fleet averages are just silently wrong. And locking every insert fixes the race only by making ten senders queue behind each other.
The fix:
  Make ingest lock-free: each arriving reading is a single atomic enqueue, nothing else. All grouping by depot and sensor type is deferred to a one-thread drain at flush time.
Proven, not hoped: an automated stress test hammers the intake with 32 concurrent threads writing 200 readings each, and after the drain every one of the 6,400 readings is accounted for, with zero lost.

## Slide 6: Takeaways
Intelligence at the edge: the fog gateway windows, aggregates and alerts right next to the vehicles, while the cloud stores compact per-window summaries, not raw sensor noise.
Serverless where it scales: Amazon SQS, AWS Lambda and DynamoDB absorb the fleet's writes with no servers to size, patch or babysit.
Verified, then portable: 130 automated tests, an end-to-end verified pipeline, and a single scripted step from the local run to AWS.
Thank you. Questions?