## Slide 1
EV Charging Network Monitoring
Nemi Ishwarlal Vikani · X24303046
Conditions at a charging hub move in seconds — a manual round or an hourly poll leaves an overloaded or overheating bay unnoticed for the whole gap between checks.
Current > 32 A
Station > 45 °C
Grid draw > 80 kW
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Edge to Cloud
Hub sensors
10 · 2 hubs · 5 metrics
Fog node
windows · 4 rules
Amazon SQS
1 aggregate / window
AWS Lambda
python3.12 ingest
DynamoDB
durable store
API GW + S3
live dashboard
Raw readings stay at the edge; the fog node sends one aggregate per sensor per window, so alerts fire next to the hardware.

## Slide 3
Live Demo
ecn-frontend-350600740537.s3.us-east-1.amazonaws.com
1
Two hubs, five charging metrics
Current, battery charge, temperature, grid load and session time live for both hubs, freshest reading a few seconds old.
2
Two safety alerts on hub-1
Overheat risk and grid strain are both firing live on hub-1, each raised at the fog node the moment its window crossed.
3
Real data, climbing
The stored-record count runs from 26 to 289 across the verification window, confirming genuinely live data.
Switch to the live dashboard here — backup video ready.

## Slide 4
Hardest Part — one Flask app, two front doors
Problem
The dashboard is a Flask application, but API Gateway invokes a Lambda with a proxy event, not an HTTP request — so the same code had to answer in both worlds. Re-declaring every route for Lambda would drift from the local server over time, and a third-party adapter would add a dependency to maintain.
Solution
A small hand-rolled bridge turns the API Gateway proxy event into a standard Python web-server environment and invokes the existing Flask app unchanged, with a cross-origin header on every response. A pre-deployment audit also confirmed the recurring pitfalls — paginated counting, batched publishing and credential handling — were already correct.