## Slide 1
Water Treatment Utility Monitoring
Rakesh Kunchala · X25176862
Treatment quality moves second by second, and a momentary pressure drop can mean a hydraulic fault even when the daily mean looks perfectly healthy — transient events vanish into averages.
Pressure < 2 bar (min)
Chlorine < 0.2 ppm
10 s window score
Fog & Edge Computing (H9FECC) · deployed live on AWS

## Slide 2
What I Built — Intake to Dashboard
Plant sensors
10 · 2 plants
Fog node
10 s windows · gates
Amazon SQS
1 summary / window
AWS Lambda
nodejs20 ingest
DynamoDB
time-series store
API GW + S3
compliance board
Every ten-second window is scored as it closes, and thresholds are checked against the window minimum, never the average, so a brief dip cannot hide.

## Slide 3
Live Demo
wtu-frontend-824792629641.s3.us-east-1.amazonaws.com
1
A reading-by-plant matrix
Turbidity, pH, chlorine, flow and pressure for both plants, with compliance strips showing each against its drinking-water limit.
2
A brief pressure dip cannot hide
The low-pressure rule reads the window minimum, not the average, so a momentary drop below 2 bar is flagged even when the mean looks healthy.
3
Cross-plant trends, live
The trend charts run both plants side by side, so an under-chlorination drift is visible as it develops.
Switch to the live dashboard here — backup video ready.

## Slide 4
Hardest Part — proving the queue drains under a burst
Problem
Normal traffic is one summary every ten seconds; to claim scalability I fired 2,000 messages at the queue from 32 parallel workers. But from outside, a non-empty queue is ambiguous — a slow consumer and a dead one look identical — and the emulator runs the Lambda in a single container, so drain time swings wildly and a naive pass/fail test either flakes or lies.
Solution
A two-tier check: first assert the queue really absorbed the burst, then require either a full drain in time or a backlog strictly below the post-burst peak. A strictly decreasing backlog proves the consumer is alive and working, not stalled — real progress, not a guess.